## Slide 1: Chord RECOGNITION
YUJIA QIU

## Slide 2: INTRO
This project is to process input audio files and recognize one of 12 major chords, i.e., C, C#, … B.
The whole project is mainly based on FFT and the Maximum Likelihood method, to find the three most likely notes in the input audio.
Based on these notes, a decision is made about whether the file contains a valid chord and if so which chord it is.
Piano triad chords were used to test the algorithm. The algorithm was implemented as the C program chordrecog which ran under Unix.

## Slide 3: METHOD
FFT -- Fast Fourier Transform
8192(2^13) samples
C4, E4, G4
f0: 261.626, 329.628, 391.995,
2*f0: 523.252 659.256 783.99

## Slide 4: method
Maximum-Likelihood Estimation
Every note is the combination of several harmonic frequency, including f0 (fundamental frequency), 2*f0, 3*f0…
A weight for each nth harmonic of f0 is assumed to be 1/n.

## Slide 5: output
The notes match C major, it is assumed the input audio is in fact a C major chord.
Sometimes, because of surrounding noises, the result may not be accurate. But because the three notes are contained in the C major chord, we still assume it’s a C major chord.
There are only two notes that match the C chord, which means this may or may not be a C chord.
There is only one note matches, which means input audio cannot be a chord

## Slide 6: RESULT
12 major chords from Apple app GarageBand
12 major chords from a piano in the Music Building
Three random notes (non-chord) as the input from Apple app GarageBand
The results for all of these sound file input were 100% correct.

## Slide 7: Limitation
There are only 12 chords in my database
Only triad chords are considered
Test case is limited

## Slide 8: Code -- database

## Slide 9: Thank you!